## Slide 1
APSSDC (IoT with Raspberry Pi)

## Slide 2
Raspberry Pi

## Slide 3
The Raspberry Pi is a low cost, credit-card sized computer that plugs into a computer monitor or TV, and uses a standard keyboard and mouse.
The Raspberry Pi was created in Febuary 2012 by the Raspberry Pi Foundation
Official site: www.raspberrypi.org
What isRaspberry Pi

## Slide 4: Arduino & Raspberry Pi Differences
SL No. | Raspberry Pi | Arduino
1 | It is a mini computer with Raspbian OS. It can run multiple programs at a time. | Arduino is a microcontroller, which is a part of the computer. It runs only one program again and again.
2 | It is difficult to power using a battery pack. | Arduino can be powered using a battery pack.
3 | It has 64 Bit Processor | It has 8 Bit Controller
4 | It has 900MHz Processor, (1.2GHz for Pi 3) | It has 16MHz .
5 | It is expensive | It is available for low cost.
6 | Raspberry Pi can be easily connected to the internet using Ethernet port and USB Wi-Fi dongles. | Arduino requires external hardware to connect to the internet and this hardware is addressed properly using code.

## Slide 5
Raspberry Pi Models
Raspberry Pi 3 Model B
Raspberry Pi 2 Model B
Raspberry Pi 1 Model B+
Raspberry Pi 1 Model B
Raspberry Pi 1 Model A
Raspberry Pi 1 Model A+
Raspberry Pi Zero W
Raspberry Pi Zero

## Slide 6
Raspberry Pi Models

## Slide 7: Raspberry Pi 3 Technical Specifications
64-bit quad-core ARMV8 CPU 1.2GHz
1GB RAM
Onboard WIFI - BCM43143
Bluetooth 4.1 (Bluetooth Low Energy - BLE)
40 Pin GPIO
4 USB-2 ports
4-pin stereo output and Composite video output
Full HDMI Port
Raspberry Pi camera port CSI
Raspberry Pi 7"" touch screen display port
Micro SD Socket
Updated power up to 2.5 amp
Power and Actions indications LEDs

## Slide 8
Raspberry Pi 3 Model B

## Slide 9: BOARD DESCRIPTION

## Slide 10
64-bit quad-core ARMV8 Broadcom BCM 2837 CPU 1.2GHz
LAN Controller

## Slide 11
Storage
SD Card Slot

## Slide 12
Raspberry Pi Networking-Via Ethernet

## Slide 13
Raspberry Pi Networking-Via WiFi
Raspberry Pi-3 Built in WiFi

## Slide 14
CSI(Camera Serial Interface) Port
The Raspberry Pi has a Mobile Industry Processor Interface (MIPI) Camera Serial Interface Type 2 (CSI-2), which facilitates the connection of a small camera to the main Broadcom BCM2835 processor

## Slide 15
The Raspberry Pi connector S2 is a display serial interface (DSI) for connecting a liquid crystal display (LCD) panel using a 15-pin ribbon cable.
The mobile industry processor interface (MIPI) inside the Broadcom BCM2837 IC feeds graphics data directly to the display panel through this connector
DSI(Display Serial Interface) Port

## Slide 16: PIN DESCRIPTION

## Slide 17
Raspberry Pi Pins
GPIO Pins: 3,5,7,8,10,11,12,13,15,16,18,19,21,22,23,24,26,27,28,29,31,32,33,35,36,37,38,40
GND Pins: 6,9,14,20,25,30,34,39
3.3V Pins: 1,17
5V Pins: 2,4

## Slide 18
Equipment Needed to set up Raspberry Pi

## Slide 19
Equipment Needed..
A Monitor with VGA/HDMI cable
Power supply
USB Keyboard and Mouse
SD Card

## Slide 20
Setup..

## Slide 21
Software setup..
Select the Operating System
Download the Operating system
Format SD card
Burn(Flash) the SD card

## Slide 22
Operating system
NOOBS
Raspbian
Raspberry Pi Desktop
Thirty Party operating system-Ubuntu Mate
-Windows IoT core
-PINET
                -RISC OS

## Slide 23
Operating systems included in NOOBS are
Raspbian
Pidora
LibreELEC
OSMC
RISC OS
Arch Linux

## Slide 24
Format SD card…
Sdcard.org->Download SD card formatter
Install the software

## Slide 25
NOOBS(New Out of Box Software)
NOOBS—NOOBS
-NOOBS LITE

## Slide 26
RASPBIAN
RASPBIAN STRETCH WITH DESKTOP
RASPBIAN STRETCH LITE

## Slide 27
BURN(FLASH) O.S
ETCHER-Software(etcher.io)

## Slide 28: Pi-top